## Slide 1
Harmful Agal Blooms​
HABS​
Ann Loree, MSPH, CHO, REHS/RS, CP-FS, SE, SI
September 10, 2025
A local Challenge from Wayland Massachusetts

## Slide 2
What are Harmful Algal Blooms (HABS)?

## Slide 3
Various
Algae types

## Slide 4
What Causes HABs to Grow?
Warm weather
  Sunlight
  Environmental Conditions:
  Sunlight
  Warm temperatures
  Warm water
  Stagnant or slow moving water
  Water fowl
  Excess Nutrients:
  Nitrogen and phosphorus
  Fertilizer
  Human and animal waste
  Failed Septic Systems
  sunlightnutrients
Sto
  Warm weather
  Sunlight
  Excess nutrients
  Stagnant/slow-moving waters
Specific factors behind each bloom vary because every waterbody is different.
Two most common factors: Phosphorus and Nitrogen, which are found in fertilizers and human/animal waste.
Septic system effluent leaks and geese, duck, and dog droppings are causative.
  moving waters
Specific factors behind each bloom vary because every waterbody is different.
Two most common factors: Phosphorus and Nitrogen, which are found in fertilizers and human/animal waste.
Septic system effluent leaks and geese, duck, and dog droppings are causative.
Notes: When do they grow?
What influences their growth?
Certain environmental conditions, such as warm weather, sunlight, excess nutrients, and stagnant/slow-moving waters help cyanobacteria grow faster. Specific factors behind each bloom vary because every waterbody is different. However, two of the most common factors are phosphorus and nitrogen, which are found in fertilizers and human/animal waste.
Septic system effluent leaks and geese, duck and dog droppings are causative.

## Slide 5
Hydrogeology of Wayland, Massachusetts
2 ponds in neighboring towns cascade in series into North Pond, Lake Cochicuate.
HABs bloom flow in the same direction from one pond into the other.
In 2023 Wayland Board of Health chose to test the water before closing the bathing beach.
Notes: Lake Cochicuate Image Link: https://live.staticflickr.com/8661/28376826640_30bc4d93bb_b.jpg

## Slide 6
Massachusetts
Environmental Protection
Agency
Notes: Massachusetts Department of Environmental Protection Demonstrates proper sampling

## Slide 7
Testing for Microcystins
Abraxis Microcystins Test Strip Method
8 step bench assay test
Test strip
AbraScan Reader
Notes: Method we chose to use for Testi
Abraxis Microcystins Test Strip Method
6 step bench assay test
Test strip
Abrascan Readerng for Microcystin

## Slide 8
Abraxis Microcystins Test Strip Method

## Slide 9: Pipette 1 ml of sample into lyse vial

## Slide 10: Shake the vial for two minutes, let stand for 8 minutes

## Slide 11: Add reagent paper

## Slide 12: Shake for two minutes

## Slide 13: Let vial stand and cook for 8 minutes

## Slide 14: Remove .1 ml with the micro pipette to a microcentrifuge tube

## Slide 15: Swirl the microcentrifuge tube for 30 seconds

## Slide 16: Test strip is placed into microcentrifuge tube arrows down for 10 minutes

## Slide 17: Remove test strip and let sit for 5 minutes

## Slide 18: Strip goes into the black jacket

## Slide 19: Position the test strip so test line is next to indents on the black jacket

## Slide 20: Insert the black jacket and test strip arrows down

## Slide 21: Enter sample ID number into AbraScan

## Slide 22: Processing sample

## Slide 23: Microcystins Not Detected

## Slide 24: Blue bracket is control line Green bracket is test line Both Lines must be in respective brackets to be valid

## Slide 25: Testing is Key
Know if you have a rising toxin situation in your recreation waters
Fresh water situation can change overnight
If you rely solely on visual, risk missing it!

## Slide 26
Lessons Learned
You cannot always tell by looking at it!
Find a method that goes beyond observation.
Plan for time to work out the technology.

## Slide 27
Thank you!
Ann Loree MSPH, CHO, REHS/RS, CP-FS, SE, SI
Regional Health Agent
Great Meadows Public Health Collaborative
loreea@sudbury.ma.us